## Slide 1: Lab 4
RGB LED & KEYPAD & 7-Segment

## Slide 2: Lab4.1
按下 R 鍵, random產生一個二位數N(00~99), 並顯示在 右邊兩個7-segment 上.
按鍵對應的模數運算如右下表所示，按下一次只會執行一次.
=>餘數會顯示在最左邊的7-segment 上
e.g., 右圖為產生的亂數 17, 按下“%2”鍵後的顯示結果
按下 C 鍵=> 7-segment 全暗, 重新開始.
%2 |  | R
%3 |  | 
%5 |  | C

## Slide 3: Lab4.2
模擬路口紅綠燈的動作
一般情況下，以「綠燈(G) 8 秒」->「黃燈(Y) 5 秒」->「紅燈(R) 13 秒」進行循環。
按下 G/Y/R 立即切換 綠/黃/紅 燈，並在七段顯示器上顯示該燈號的初始秒數。
秒數以每一秒遞減方式顯示，當數字遞減至1時，下一秒顯示下一個燈號的初始秒數。
按下 + ，當下剩餘秒數增加 5 秒。
G | Y | R
 |  | +

## Slide 4
and

## Slide 5: 參考資料:產生亂數
int main(){
int count = 0;
while(1){
count++;
...
// when key=7
srand(count);
}
}
Why srand(time(NULL)) 不能用?
→ time Undefined
→ 自己產生種子

## Slide 6: 紅綠燈 ver. 1
int main(){
int greenDuration = 8, yellowDuration = 5, redDuration = 13;
int timer = greenDuration;
int step = 0;
int state = 0;
while(true){
// Assume that the following function takes 1ms during runtime.
Segment_show4DigitNumber(timer); // Decrease 1 per approximate 1 second.
step = (step + 1) % 1000;
if(step == 0){
timer -= 1;
if(timer <= 0){
switch(state){
case 0: timer = yellowDuration; state = 1; break;
case 1: timer = redDuration; state = 2; break;
case 2: default: timer = greenDuration; state = 0; break;
}
}
}
}
}
gonna

## Slide 7: 紅綠燈 – 改進方式
狀態不容易追蹤 -> 使用 enum。
有關聯的變數零散 -> 使用 struct。
讓 main 結構清晰 -> 使用 function & pointer to struct 。
目的：增加程式碼的可讀性與可維護性。
give

## Slide 8: 紅綠燈 ver. 1 改動處
int main(){
int greenDuration = 8, yellowDuration = 5, redDuration = 13;
int timer = greenDuration;
int step = 0;
int state = 0;
while(true){
// Assume that the following function costs about 1ms during runtime.
Segment_show4DigitNumber(timer); // Decrease 1 per approximate 1 second.
step = (step + 1) % 1000;
if(step == 0){
timer -= 1;
if(timer <= 0){
switch(state){
case 0: timer = yellowDuration; state = 1; break;
case 1: timer = redDuration; state = 2; break;
case 2: default: timer = greenDuration; state = 0; break;
}
}
}
}
}
Using `enum` is better.
Make a function to countdown and change to next state.
Using `struct` is better.

## Slide 9: 紅綠燈 ver. 2
enum State {GREEN, YELLOW, RED};
struct TrafficSignal{
enum State state;
int greenDuration, yellowDuration, redDuration;
int timer;
}; void TrafficSignal_initialize(struct TrafficSignal *ts, int greenDuration, int yellowDuration, int redDuration){
ts->state = GREEN;
ts->greenDuration = greenDuration;
ts->timer = greenDuration;
ts->yellowDuration = yellowDuration;
ts->redDuration = redDuration;
} void TrafficSignal_countDown(struct TrafficSignal *ts){
ts->timer -= 1;
if(ts->timer == 0){
switch(ts->state){
case GREEN: ts->state = YELLOW; ts->timer = ts->yellowDuration; break;
case YELLOW: ts->state = RED; ts->timer = ts->redDuration; break;
case RED: default: ts->state = GREEN; ts->timer = ts->greenDuration;
}
}
}
up

## Slide 10: 紅綠燈 ver. 2
int main(){
struct TrafficSignal ts;
int step = 0;
TrafficSignal_initialize(&ts, 8, 5, 13);
while(true){
// Assume that the following function costs about 1ms during runtime.
Segment_show4DigitNumber(ts.timer);
step = (step + 1) % 1000;
if(step == 0){
TrafficSignal_countDown(&ts);
}
}
}
never